Ebola Virus Antigen Nasal

One-Step Test Kit

### Intended Use

Ebola Virus Test is a lateral flow immunoassay for rapid, qualitative detection of Ebola virus antigen directly from nasal swab, nasopharyngeal swab, nasal wash and/or nasal aspirate specimens. Test results are available in less 10 minutes or less. The test is intended for use as an aid in the diagnosis of Ebola Virus infection.

Procedure

Prior to use, bring all test components and patient samples to room temperature.

- Carefully insert the sterile swab into the nostril and into the nasopharynx about 2 inch (very important step) and gently roll the swab at least 2 times.

- Open the cap of the extraction buffer vial and Place the swab sample into the Extraction buffer glass vial. Roll the swab at least 3 times while pressing the head against the bottom and the side of the glass vial.

- Roll the swab head against the inside of the Extraction buffer glass vial as you remove it. Dispose of the used swab in accordance to your biohazard waste disposal protocol. Screw the cap back to the extraction buffer.

Note:  A sterile swab is passed

gently through the nostril and  into

the nasopharynx.(about 2 inches)

Insert swab up to this point.

4.Add 2 drops of extraction buffer to the sample well of the device and read the results at 10 min.

INTERPRETATION OF RESULTS

Positive Result:

If both the Control band (C line) and the Test band (T line) appear, the result indicates that the virus  is detected and the result is positive.

Negative Result:

If the Control band (“C line) appears, with no Test band (“T line). The result is negative.